## Slide 1
Yiping Shao
Division of Medical Physics and Engineering
Department of Radiation Oncology
University of Texas Southwestern Medical Center
Radiology Research Day 2021 Nov 17, 2021
Advanced PET imaging
for potentially breakthrough
functional image-guided radiotherapy applications
Radiation Oncology

## Slide 2
Outline: Three research projects we are working on:
Develop PET to expand the small animal RT research capability
Apply on-line PET imaging for improving particle (e.g. proton) therapy accuracy
Investigate using TOF PET to enable practical real-time marker-less tumor motion tracking - with targeted performance far beyond Reflexion’s X1 PET-Linac
Current technologies
Existing technical gaps that impede the new and novel clinical/preclinical RT applications
New technologies we are developing to fill the gaps and enable the new and novel RT applications
Introduction
Lab: Nuclear Imaging Technology Development and Application Lab
Research focus: Develop and apply advanced PET imaging technology to enable novel functional image-guided
photon and particle radiotherapy applications

## Slide 3
Integrated small animal PET/CT/RT for preclinical radiation research
Current technology:
Technical gap:
moving bed
X-ray detector
X-ray tube
CT image guidance only
No PET functional image guidance

## Slide 4
Integrated PET/CT/RT
Onboard imaging for high precision
Streamline imaging/radiation processes
Dynamic imaging & motion-compensation
Potential solutions
Separated PET/CT and CT/RT
Logistical issues
Image co-registration
Limited imaging options
Notes: I am gonna start off by introducing our project,
which is to embed a high-resolution PET into a small animal irradiator. So that researchers can do PET/CT imaging and radiation treatment in a same machine.
Without moving the couch and the animal from one site to another, the position change of organs and tissues is reduced and also to minimize the realignment error.

## Slide 5
New enabling technology
Linear stage
moving bed
PET
X-ray detector
X-ray tube
Development of an insert PET
(Compact and lightweight)
Integrate PET with CT/RT
Evaluate PET/CT/RT

## Slide 6
A PET detector panel
Scintillator array
Image FOV: 8cm & 3.5cm
Light weight: 6.5 kg
PET
X-ray tube
X-ray detector
1.0 mm
1.35
0.75
1.7
2.0
2.4
PET phantom image
detector
Readout electronics

## Slide 7
CT acquisition
PET acquisition
Mouse with ~21 g weight
Subcutaneous injected tumor cell at the thigh
Tumor size ~3.9 mm diameter and ~7.1 mm long
~5.6 kBq 18FDG injection, 30 min uptake, ~25 min acquisition
mouse

## Slide 8
Onboard CT, PET and PET/CT images
(trans-axial view)
(coronal view)
(sagittal view)

## Slide 9
Image line profiles

## Slide 10
Whole-body animal PET/CT images